## Slide 1
Binary Neural Net Design Contest
Suggestions
Greg Stitt
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Neuron Processor (NP) Interface
xnor
popcount
x[0..Pw-1]
threshold
y
Interface should enable pipelinine/streaming
Data inputs: Pw weights (w), Pw inputs (x), threshold
  Threshold can be 32 bits, but better to have it sized for the max popcount (e.g., $clog2(MAX_NEURON_INPUTS+1))
Control inputs: valid_in, last/eof
  valid_in specifies when w and x are valid
  last/eof asserted to specify the final input for a neuron
    Processor used by many neurons, needs to know when one ends and begins
Data outputs: 1-bit “activation” output (y), multi-bit popcount
  Popcount will remain disconnected in all but the output layer
    Also useful for debugging hidden layers
  Popcount should match threshold bit width
Control outputs: valid_out
  Specifies validity of y and popcount output
w[0..Pw-1]
+
>=
popcount
*actual architecture will be more complex
last
valid_in
valid_out
control

## Slide 3: Neuron Processor (NP) Interface
e.g. 2 neurons, each with 4 inputs
  PW = 2
    (2 beats per neuron)
  Input = 0110
  Neuron 0
    Weights: 1011
    Threshold: 2
  Neuron 1
    Weights: 0010
    Threshold: 1
10
11
xnor
popcount
y
+
>=
popcount
valid_out
control
2
1
0
x
w
last
valid_in
0
Neuron 0: beat 0
1
0

## Slide 4: Neuron Processor (NP) Interface
e.g. 2 neurons, each with 4 inputs
  PW = 2
    (2 beats per neuron)
  Input = 0110
  Neuron 0
    Weights: 1011
    Threshold: 2
  Neuron 1
    Weights: 0010
    Threshold: 1
01
10
xnor
popcount
y
+
>=
popcount
valid_out
control
2
1
1
x
w
last
valid_in
0
Neuron 0: beat 1
0
1

## Slide 5: Neuron Processor (NP) Interface
e.g. 2 neurons, each with 4 inputs
  PW = 2
    (2 beats per neuron)
  Input = 0110
  Neuron 0
    Weights: 1011
    Threshold: 2
  Neuron 1
    Weights: 0010
    Threshold: 1
xnor
popcount
y
+
>=
popcount
valid_out
control
2
x
w
last
valid_in
1
Neuron 0: output
0 (resets on last)
1
0

## Slide 6: Neuron Processor (NP) Interface
e.g. 2 neurons, each with 4 inputs
  PW = 2
    (2 beats per neuron)
  Input = 0110
  Neuron 0
    Weights: 1011
    Threshold: 2
  Neuron 1
    Weights: 0010
    Threshold: 1
10
10
xnor
popcount
y
+
>=
popcount
valid_out
control
1
1
0
x
w
last
valid_in
0
Neuron 1: beat 0
2
0

## Slide 7: Neuron Processor (NP) Interface
e.g. 2 neurons, each with 4 inputs
  PW = 2
    (2 beats per neuron)
  Input = 0110
  Neuron 0
    Weights: 1011
    Threshold: 2
  Neuron 1
    Weights: 0010
    Threshold: 1
01
00
xnor
popcount
y
+
>=
popcount
valid_out
control
1
1
1
x
w
last
valid_in
0
Neuron 1: beat 1
1
2

## Slide 8: Neuron Processor (NP) Interface
e.g. 2 neurons, each with 4 inputs
  PW = 2
    (2 beats per neuron)
  Input = 0110
  Neuron 0
    Weights: 1011
    Threshold: 2
  Neuron 1
    Weights: 0010
    Threshold: 1
xnor
popcount
y
+
>=
popcount
valid_out
control
1
x
w
last
valid_in
1
Neuron 1: output
0 (resets on last)
3
1

## Slide 9: Layer Architecture
I strongly recommend using separate NPs for each layer
  Not best for all use cases, but much easier to implement
Each layer i will have:
  PW,i parallel inputs and weights, PN,i neuron processors
Neuron Processor 0
Threshold RAM0
Weight RAM0
Input Buffer
Neuron Processor 1
. . . . . . . . . . . . . .
Each processor has its own separate weight and threshold RAM
PW
Threshold RAM1
Weight RAM1
PW
PN-1
Inputs fan-out to all neuron processors
PW
. . . . . . .
Outputs from previous layer (or inputs if first hidden layer)
Configuration Controller
Writes data from configuration manager into appropriate RAM

## Slide 10: Layer Architecture
Each layer i can have its own PN,i and PW,i
  But, PN,i should match PW,i+1
  i.e., layer i generates PN,i bits per cycle, layer i+1 should consume the same amount
    If PN,i < PW,i+1, layer i+1 frequently waiting for data (slow producer bottleneck)
    If PN,i > PW,i+1, layer i+1 constantly backpressures layer i (slow consumer bottleneck)
    Plus, both require width conversion logic
I suggest you initially use same PN and PW across all layers
  Greatly simplifies configuration manager
  e.g., my initial solution set PN = PW = 8 in all layers
Once you have that working, support different values in each layer
  Main challenge: configuration manager must support outputting of weights of different widths
  e.g., PW,0=16, PW,1=8, PW,2=4
    Configuration manager must be able to pack 8-bit weights provided from configuration stream into 16, 8, and 4-bit groups depending on the layer

## Slide 11: Layer Architecture
Convention I use in latest testbench:
  Single PW (PARALLEL_INPUTS) specifies parallel inputs to 1st hidden layer
  One PN for each non-input layer (PARALLEL_NEURONS[LAYERS])
  Can derive PW,i for each layer i from PN,i-1
    Layer 0 has PARALLEL_INPUTS parallel inputs
    Layer 1 has PARALLEL_NEURONS[0] parallel inputs
    Layer 2 has PARALLEL_NEURONS[1] parallel inputs
    Etc.
After you support different PN in each layer, you can “load balance”
  Ideally, all layers should take the same amount of time
    If not, the design is not Pareto-optimal
  Figure out the slowest layer in the BNN
    Add more parallelism for that layer to improve performance
    Or, reduce resources in other layers to improve resource utilization
Stress test individual layer with different numbers of inputs, parallel inputs, parallel neurons, etc.
  Testbench will imitate configuration manager
  Verify activation and popcount outputs

## Slide 12: BNN Architecture
Before creating the final bnn_fcc architecture, make a pure BNN architecture
  Inputs already binarized, no argmax
  Literally just concatenates all layers as required by topology
  No configuration manager, just the interface required by each layer
  Make testbench that imitates configuration manager
    Forces you to decide how manager will provide data
Stress test:
  Numerous topologies
  Different PW and PN combinations
  Downstream backpressure
  Gaps in input stream
Layer 0
Layer 1
Layer N-1
Binary Inputs
Activation
Popcount
. . . . .
Config
Config
Config

## Slide 13: BNN_FCC Architecture
Combine the BNN with binarization, argmax, and configuration manager
Use provided testbench to verify loading of weights and thresholds to each layer of the BNN
Stress test with small topologies
Increase topology size and parallelism
Binarization
BNN
Argmax
Pixel Inputs
Classification
Configuration Manager
Configuration Stream

## Slide 14: Parsing Challenges
Parsing challenge: weights likely change between neurons in middle of bus
  Can’t statically divide weights into separate neurons
Configuration bus width (B), # of weights for a given neuron (N)
Example: B = 64, N = 48
  Neuron 0 weights start at bit 0 in beat 0, ends in bit 47 of beat 0
  Neuron 1 weights start at bit 48 in beat 0, ends in bit 31 of beat 1
  Neuron 2 weights start at bit 32 of beat 1, ends at bit 15 of beat 2
  Neuron 3 weights start at bit 16 of beat 2, ends at bit 63 of beat 2
  Etc.
High-performance solution:
  Barrel shift register to align each neuron’s weights with position 0
  Not easy to do efficiently, positions change in every layer
Good news: no performance constraint on configuration
  Easier solution: asymmetric FIFO to convert bus stream into individual bytes

## Slide 15: Parsing Challenges
Simple (but slow) solution: Convert B-bit config stream into stream of bytes
  Parse the individual bytes
Asymmetric FIFOs exist for this situation
  Different widths for read (8) and write (B) port
Problem: what if payload is not aligned with B bits?
  E.g., B = 64, payload = 6 bytes (48 bits)
  Bus provides 2 bytes that aren’t needed
Unused bytes must be ignored
  2 options:
  1) Drain extra bytes from FIFO
  2) Prevent bytes from entering FIFO (requires specialized FIFO with variable write count)
How to identify extra bytes?
  1) Use knowledge of payload size, drain FIFO after reaching payload end
  2) Use TKEEP AXI signal (specifies bytes that should be ignored)
FIFO
B
8

## Slide 16: RAM Width Conversion Challenges
Each neuron processor takes Pw weights/inputs in parallel
  Need to convert 8-bit config stream into Pw bit words for RAMs
Asymmetric FIFOs again solve this problem
A few common problems:
  If Pw > 8, you must ensure you write in multiples of Pw / 8
    Otherwise, the FIFO will remain empty
    e.g. Pw= 64, FIFO is !empty after 8 writes
    May require injection of entire padded beats
      e.g., for N = 32, config manager must write 4 extra bytes of padding to provide Pw = 64
      Padded weights should all be 1
  If Pw < 8, you might need to throw out data
    e.g. Pw= 4, FIFO provides two beats of 4 bits for every 8-bit write
    Extra bits should be ignored (same problem as last slide)
    Ignore via counter that tracks last valid Pw bits, or leverage TKEEP again
FIFO
8
Pw

## Slide 17: Misc Suggestions
Require the number of neurons in layer i to be a multiple of PN,i
  Not necessary, but non-multiples require padding and extra logic
Require inputs to BNN to be multiple of PARALLEL_INPUTS
  Again, not necessary, but requires padding of inputs
If you have everything working, you can then add more flexibility
  Biggest limitation is that SFC topology has 784 inputs
  Not a multiple of all powers of 2